## Slide 1
RISC-V Microcontroller
On Cmod-A7-35T
Developed by Wei-Feng Huang, DICLAB, NCKU

## Slide 2: Outline
FPGA Selection and Spec
Overview Microcontroller / AXI Mapping
GPIO / Interrupt System / Timer & PWM / XADC / UART
Memory Hierarchy
Hardware Report
Software Design Flow
Standalone Boot Sequence

## Slide 3: Outline
FPGA Selection and Spec
Overview Microcontroller / AXI Mapping
GPIO / Interrupt System / Timer & PWM / XADC / UART
Memory Hierarchy
Hardware Report
Software Design Flow
Standalone Boot Sequence

## Slide 4: FPGA Selection and Spec
Board: Cmod-A7-35T
Chip: xc7a35tcpg236-1
Breadboard-friendly 48-pin DIP connector
All 48 DIP pins at LVCMOS33 (3.3 V logic level)
No series resistors — direct connection to FPGA I/O
Analog pins: 0–3.3 V input, scaled to 0–1 V via on-board voltage divider
TWD: 3,092

## Slide 5: FPGA Selection and Spec
NOR Flash 4MB:
Micron-N25Q032A (32Mbit / 4MB) or
Macronix-MX25L3233FZBI-08G/Q (32Mbit / 4MB)
SRAM 512KB:
IS61WV5128BLL-10BLI (512KB)
FPGA:
XC7A35T-1CPG236C
PMOD
UART / JTAG
FTDI FT2232HQ
UART / JTAG
Micro-USB

## Slide 6: FPGA Selection and Spec
Filter Capacitor
DIP pin:
Notes: 1. 降壓分壓：2.32kΩ 與 1kΩ 電阻負責將外部訊號（如 3.3V）按比例縮小至 XADC 安全可測的 0~1V 範圍。
2. 戴維寧等效電阻 (ADx_P)：將電源短路接地後，分壓電阻視為並聯。ADx_P 端看出去的等效阻抗為 (2.32kΩ // 1kΩ) + 140Ω ≈ 838Ω。
Adx_N 則為845直接接地
3. 阻抗匹配 (ADx_N)：ADx_N 端直接串聯 845Ω 電阻接地，目的是與 ADx_P 端的 838Ω 達成極度接近的阻抗匹配。
4. 核心目的：兩端阻抗平衡可以完美抵銷 ADC 內部直流偏置電流（DC Bias Current）所造成的壓降誤差，大幅提升差分測量的精準度。
在這裡鍵入方程式。5. 高輸入阻抗：XADC 測量端阻抗極高，實際流入的電流微乎其微（nA等級），在外部電阻上產生的電壓降極小，幾乎不影響量測。
6. 差分相減抵銷誤差：即便有微小的偏置電流，因為 P 端 (838Ω) 與 N 端 (845Ω) 阻抗極度匹配，兩端產生的誤差電壓相等。XADC 測量差分電壓（P減N）時，此誤差會被完美抵銷。
1. 降壓分壓：2.32kΩ 與 1kΩ 電阻負責將外部訊號（如 3.3V）按比例縮小至 XADC 安全可測的 0~1V 範圍。
2. 戴維寧等效電阻 (ADx_P)：將電源短路接地後，分壓電阻視為並聯。ADx_P 端看出去的等效阻抗為 (2.32kΩ // 1kΩ) + 140Ω ≈ 838Ω。
Adx_N 則為845直接接地
3. 阻抗匹配 (ADx_N)：ADx_N 端直接串聯 845Ω 電阻接地，目的是與 ADx_P 端的 838Ω 達成極度接近的阻抗匹配。
4. 核心目的：兩端阻抗平衡可以完美抵銷 ADC 內部直流偏置電流（DC Bias Current）所造成的壓降誤差，大幅提升差分測量的精準度。
"在這裡鍵入方程式。"5. 高輸入阻抗：XADC 測量端阻抗極高，實際流入的電流微乎其微（nA等級），在外部電阻上產生的電壓降極小，幾乎不影響量測。
6. 差分相減抵銷誤差：即便有微小的偏置電流，因為 P 端 (838Ω) 與 N 端 (845Ω) 阻抗極度匹配，兩端產生的誤差電壓相等。XADC 測量差分電壓（P減N）時，此誤差會被完美抵銷。

## Slide 7
FPGA Selection and Spec
Overview Microcontroller / AXI Mapping
GPIO / Interrupt System / Timer & PWM / XADC / UART
Memory Hierarchy
Hardware Report
Software Design Flow
Standalone Boot Sequence

## Slide 8: Overview Microcontroller
MicroBlaze V
Debug
Module
AXI GPIO * 7
AXI Timer
AXI Interconnect (BUS)
On-Board
LED /
RGB LED /
Button
AXI UART
16550
JTAG
Local Memory
Bus
Data Mem /
Inst Mem /
Shared 128KB
GPIO pin*28
GPIO_A0 ~ GPIO_A6
……
GPIO_D0 ~ GPIO_D6
Interrupt pin*4
INTR_0
……
INTR_3
AXI UART
16550 * 2
USB-UART / UART_RX / UART_TX
AXI
EMC
AXI Timer
SRAM
512KB
AXI Timer
* 6
PWM_0 ~ PWM_2
AXI
Quad-SPI
Flash
4MB
XADC
ADC_0 / ADC_1

## Slide 9: Memory-Mapped I/O vs SFR
Memory-Mapped I/O (MMIO):
  Peripherals are mapped into the memory address space
  Accessed using normal load/store instructions
  Easy to integrate and extend (add new devices by assigning new addresses)
SFR (Special Function Registers) in traditional MCUs (e.g., PIC):
  Peripheral control uses dedicated special registers
  Often requires bank selection / bit-level control
  Less flexible when scaling to more peripherals

## Slide 10: AXI Mapping
Although each peripheral is mapped to a memory address range, this address region does not correspond to physical RAM.
Instead, AXI address decoding and routing logic forwards these transactions to the target peripheral’s register interface (MMIO).

## Slide 11: Overview Microcontroller
Processor: MicroBlaze RISC-V, 32-bit, Single Core
Clock: 100 MHz (12 MHz OSC → Clocking Wizard PLL)
ISA Extensions: RV32IM_Zba_Zbb_Zbc_Zbs
Local Memory: 128 KB BRAM (ILMB + DLMB)
Cache: Disabled (I-Cache & D-Cache both off)
Debug: MDM JTAG — breakpoints, register, memory R/W
Interrupt: AXI INTC, 6 sources (3 Timer + 2 UART + 1 GPIO)

## Slide 12
FPGA Selection and Spec
Overview Microcontroller / AXI Mapping
GPIO / Interrupt System / Timer & PWM / XADC / UART
Memory Hierarchy
Hardware Report
Software Design Flow
Standalone Boot Sequence

## Slide 13: GPIO
AXI Interconnect (BUS)
gpio_B_0_6
gpio_A_0_6
gpio_C_0_6
INT_0_3
board_button
board_rgb
board_led_2bits
gpio_D_0_6

## Slide 14: Timer & PWM
AXI Interconnect (BUS)
AXI Timer
* 3
RISC-V
Core
AXI
Interrupt
Controller
Concat
AXI Timer
* 3
AXI Timer
* 3
irq
AXI Timer
* 3
AXI Timer
* 3
AXI Timer
* 3
PWM_0 ~ PWM_2
6 AXI Timer Instances — Two Roles:
3 × System Timers (timer_0 / timer_1 / timer_2)
Connected to AXI Interrupt Controller
Generate periodic interrupts for scheduling, timeout, or time measurement
3 × PWM Timers (PWM_0 / PWM1 / PWM_2)
Configured in PWM mode
Used for servo control (SG90)
All 6 timers are the same IP, the difference is purely in how they are used — interrupt source vs. PWM output.

## Slide 15: UART
AXI Interconnect (BUS)
AXI UART
16550
AXI UART
16550 * 2
UART_RX / UART_TX
USB-UART
2 × AXI UART 16550 Instances:
uart_USB — Console / Debug
  Connected to on-board USB-UART via Micro-USB (J3)
  No DIP pin exposed — accessed through USB cable
uart_1 — External Communication
  TX/RX routed to DIP Pin 11 / Pin 12
  Available for connecting external devices (sensors, modules, another MCU)

## Slide 16: XADC
XADC — On-chip Analog-to-Digital Converter
  Built-in 12-bit ADC inside Artix-7 FPGA
Enabled Channels (Continuous Sequencer):
  VAUX4 (DIP Pin 15) — external analog input
  VAUX12 (DIP Pin 16) — external analog input
  Temperature — on-chip die temperature
  VCCINT — core voltage monitor (1.0 V)
  VCCAUX — auxiliary voltage monitor (1.8 V)
Key Specs:
  Total conversion rate: 500 Kilo Samples Per Second (KSPS)
  Per-channel effective rate: ~100 KSPS (500K ÷ 5 channels)
  Input range: 0–1 V at FPGA pins (3.3 V on DIP pin scaled by on-board voltage divider)
  Resolution: 12-bit (4096 levels)

## Slide 17: Interrupt System
AXI Interconnect (BUS)
AXI Timer
* 3
RISC-V
Core
AXI
Interrupt
Controller
Concat
AXI Timer
* 3
AXI Timer
* 3
AXI GPIO
w intr * 3
irq
AXI UART
16550
AXI UART
16550 * 2
Interrupt handling flow (Normal Mode) :
Peripheral asserts interrupt line
Concat interrupt lines → AXI Interrupt Controller
AXI Interrupt Controller asserts IRQ → CPU
CPU jumps to fixed ISR entry point
Reads axi_intc register to identify source
Branches to corresponding handler
Handler processes the event
Clear peripheral interrupt first
Then clear axi_intc
Return from ISR, CPU resumes normal execution

## Slide 18
FPGA Selection and Spec
Overview Microcontroller / AXI Mapping
GPIO / Interrupt System / Timer & PWM / XADC / UART
Memory Hierarchy
Hardware Report
Software Design Flow
Standalone Boot Sequence

## Slide 19: Memory Hierarchy

## Slide 20
FPGA Selection and Spec
Overview Microcontroller / AXI Mapping
GPIO / Interrupt System / Timer & PWM / XADC / UART
Memory Hierarchy
Hardware Report
Software Design Flow
Standalone Boot Sequence

## Slide 21: Hardware Report

## Slide 22
FPGA Selection and Spec
Overview Microcontroller / AXI Mapping
GPIO / Interrupt System / Timer & PWM / XADC / UART
Memory Hierarchy
Hardware Report
Software Design Flow
Standalone Boot Sequence

## Slide 23: Software Design Flow

## Slide 24
Software Design Flow

## Slide 25: Software Design Flow for Debug
Two development approaches:
Xilinx Vitis + Embedded SW Libraries
  Official IDE with BSP auto-generation
  Includes drivers for all AXI peripherals (GPIO, UART, Timer, SPI, EMC)
RISC-V GNU Toolchain
  Standalone GCC cross-compiler (riscv32-unknown-elf / riscv64-unknown-elf)
  Full control over linker scripts, startup code, and register-level access
  No dependency on Xilinx toolchain
Both target the MicroBlaze RISC-V soft processor running on the Cmod A7-35T.

## Slide 26: Software Design Flow for Debug
XSDB (Xilinx System Debugger)
  Command-line debug interface over JTAG
  Connects to MicroBlaze via MDM (MicroBlaze Debug Module)
  Capabilities:
    Download ELF directly to BRAM/SRAM — no Flash needed
    Halt, step, and resume CPU execution
    Read/write memory and registers in real time
  Enables rapid code-test-fix cycles during development
  No bootloader required

## Slide 27
FPGA Selection and Spec
Overview Microcontroller / AXI Mapping
GPIO / Interrupt System / Timer & PWM / XADC / UART
Memory Hierarchy
Hardware Report
Software Design Flow
Standalone Boot Sequence

## Slide 28: Standalone Boot Sequence

## Slide 29: Issue to Address
Interrupt (GPIO / Timer)
GPIO input
uart 16550 Baud Rate 更改
XADC 五個channel讀值
QSPI 內建 Bitstream
EMC SRAM 使用
Memory Hier 設計
Standalone Boot Sequence流程